## Slide 1: Feedback on CONDUCTIX (Jay Electronique) radio tests
Carried out on 17/10/2023
Location: Training Center (Sens)
Operators: Matthieu Delefortrie
Brice Belin
18/10/2023

## Slide 2: Agenda
Conductix radio presentation
Tests functionalities
Remarks
Conclusions

## Slide 3: CONDUCTIX radio presentation
Comparison with old CAVOTEC
(not actual Face T)
01

## Slide 4: Front side
01

## Slide 5: Comparison with CAVOTEC
Actual - CAVOTEC | Tested - CONDUCTIX | Remarks
Transmitter: MC 3300 EX | Transmitter: MOKA | 
 |  | Communication: PROFIBUS DP
Receiver: xxxx: | Receiver: NEMO | 
      Logo is not the last
      No lights for arms
      selections
      Small displayed
      Nota:
      Do same tests with Profinet communication (or simulation)

## Slide 6: Tests functionalities
Comparison with old CAVOTEC
(not actual Face T)
02

## Slide 7: Comparison with CAVOTEC
Actual - CAVOTEC | Tested - CONDUCTIX | Remarks
Switch with 2 positions LED status: On = radio ON OFF = radio OFF | Button must be pressed | 
 |  | Actually we use this emergency button to STOP PUMP on Cavotec radio
 | Switch off with Emergency Stop button | 
Standbye time: 10 min | X | 
Switched off time: 15 min | Switched off time: 4 min | 
      Logo is not the last
      No lights for arms
      selections
      Small displayed
      2.1/ Switch ON / OFF radio

## Slide 8: Comparison with CAVOTEC
Actual - CAVOTEC | Tested - CONDUCTIX | Remarks
      Slewing movements
      => validated
      2.2/ Arm movements
      Outboard movements
      => validated
Left
Right
      Inboard movements
      => validated
      Coupler movements
      => Not validated
      Not works on our loan material
Forward
Back
Back
Forward
close
close
open
open

## Slide 9: Comparison with CAVOTEC
Actual - CAVOTEC | Tested - CONDUCTIX | Remarks
No DBV commands on radio Only on LCP |  | 
      DBV movements
      => validated
      2.2/ Arm movements
Back

## Slide 10: Comparison with CAVOTEC
Actual - CAVOTEC | Tested - CONDUCTIX | Remarks
Switch multi-positions Led status OFF = Not selected blinking = selected ON = Locked …. …. |  | 
      No lights for arms
      selections
      Picture displayed
      B1 = Arm 1
      2.3/ Arm status on radio
      Icone displayed
      B1 displayed
      Lock open = selected arm
      Icone displayed
      B1 displayed
      Lock close = Locked arm

## Slide 11: Remarks
03

## Slide 12: Remarks after tests
Points to be discuss:
  Confirmed or not to have 3 status per arms
    Suggestion: maybe 2 pictures are enough
      Delecte picture nr1
  Pictures are displayed in front of the main screen
    Suggestion: See if it’s possible to call other pages with same picture as upper
[1] Arm not selected | [2] Arm selected | [3] Arm Locked
[1] Main Screen | [2] Pictures called

## Slide 13: Remarks after tests
Points to be discuss:
  Emergency Stop button use to switch off radio
    Discuss with Conductix if possible, to use another button
    Suggestion:
      Press 1s on green button to switch ON
      Press more than 2s on green button to switch OFF
  Possible to add new texts or new pictures
    Suggestion
      Pump running
      Pump Stop
  Possible to connect cable on CONDUCTIX radio
    Like pendant mode on CAVOTEC radio
[1] Arm not selected | [2] Radio ON | [3] Radio OFF
Pressed Pressed |  | 

## Slide 14: Conclusion
04

## Slide 15: General conclusion
CONDUCTIX remote vs CAVOTEC remote
  CONDUCTIX remote do the same work like CAVOTEC remote
  Some points need to be discussed and improved
    Add new message
    change or improve the arm status displayed
  Some points need to be solved
    Lost information “Présence radio réception” send by Moka radio during manipulation
    How to change standby value on radio Moka
  Another day of testing will be scheduled with its improvements
    days should be defined with Training Center availibility